## Slide 1
Functional Connectivity in MEG
Rik Henson
MRC CBU, Cambridge

## Slide 2: Functional Connectivity Background
Much interest in functional connectivity in fMRI
And yet many neural interactions (e.g, coupled oscillations) occur at a timescale faster than visible by fMRI
Beyond localization: the same set of brain regions could perform different functions depending on how they interact
So, real promise of MEG/EEG is functional connectivity?

## Slide 3: Talk Overview
1. Problem of Field Spread (Volume Conduction)
2. Linear vs Nonlinear measures
3. Directed vs Undirected measures
4. Direct vs Indirect measures
5. Generative Models

## Slide 4: Field Spread Problem
Many (zero-lag) measures of functional connectivity between sensors can be spurious, i.e, reflect activity from single source
No true source connectivity
Spurious sensor connectivity
True source connectivity
True sensor connectivity
0-lag correlation
PDC (see later)

## Slide 5: Field Spread Problem
Source reconstruction reduces field spread problem…
…and allows easier comparison with fMRI connectivity
BUT spurious connections between sources can remain (“point-spread”)
…and field-spread is instantaneous (zero-lag), so some measures of connectivity between sensors are immune to field spread (e.g, time- or phase-lagged measures)
Hillebrand et al (2012) Neuroimage

## Slide 6: Different Types of Connection
Undirected, Indirect (bivariate)
Directed, Indirect (bivariate)
Directed, Direct (multivariate)
(“effective connectivity”)

## Slide 7: Cross-Correlation
Sensitive to Field-spread (when =0), Undirected, Indirect, Linear
Cross-covariance
Cross-correlation
=“lag”

## Slide 8: Coherency
Sensitive to Field-spread, Undirected, Indirect, Linear
(Fourier transform of cross-covariance)
(Magnitude-squared) Coherence
Coherency
Cross-covariance

## Slide 9
Digression on Complex Numbers
An oscillation of frequency f can be represented in terms of amplitude and phase (polar coordinates), which can also be represented by a complex number

## Slide 10: Coherence
Sensitive to Field-spread, Undirected, Indirect, Linear
(Magnitude-squared) Coherence
Coherency
Cross-covariance

## Slide 11: Imaginary Coherency
Immune to Field-spread, Undirected, Indirect, Linear
Imaginary Coherency
Coherency
Nolte et al (2004) Clin Neurophys

## Slide 12: Imaginary Coherency
A zero imaginary component implies a phase of the coherency of either 0o or 180o, which could be caused by field-spread…
Nolte et al (2004) Clin Neurophys

## Slide 13: Imaginary Coherency
A zero imaginary component implies a phase of the coherency of either 0o or 180o, which could be caused by field-spread…
Nolte et al (2004) Clin Neurophys

## Slide 14: Imaginary Coherency
…whereas a NON-zero imaginary component implies a phase of the coherency other than 0o or 180o, which can NOT be caused by field-spread
Nolte et al (2004) Clin Neurophys

## Slide 15
Digression on Analytic Signals
A signal can be represented analytically in terms of its amplitude and phase over time (within a narrow frequency band) (e.g, using Hilbert transform)

## Slide 16: Phase-related Measures
Phase-Locking Value
Phase-Lag Index
Stam et al (2007) Human Brain Mapp
Immune to Field-spread, Undirected, Indirect, Linear
PLV=0 PLV=0.5 PLV=0.75

## Slide 17
More complex coupling
Jenson & Colgin (2007) TICS
Power-Power
Phase-Phase
Phase-Freq
Phase-Power

## Slide 18: Talk Overview
1. Problem of Field Spread (Volume Conduction)
2. Linear vs Nonlinear measures
3. Directed vs Undirected measures
4. Direct vs Indirect measures
5. Generative Models

## Slide 19: Nonlinear Measures

## Slide 20: Nonlinear Measures
Cross-correlation/coherence insensitive to nonlinear dependencies

## Slide 21: Mutual Information
Sensitive to Field-spread, Undirected, Indirect, Nonlinear

## Slide 22: Mutual Information
Sensitive to Field-spread, Undirected, Indirect, Nonlinear

## Slide 23: Talk Overview
1. Problem of Field Spread (Volume Conduction)
2. Linear vs Nonlinear measures
3. Directed vs Undirected measures
4. Direct vs Indirect measures
5. Generative Models

## Slide 24: Directed Measures
(bivariate) Granger Causality
Immune to Field-spread, Directed, Indirect, Linear
Auto-regressive model to order p
(assuming mean-corrected, with residuals e)
Augmented model including past values of x (to order q)
If classical F-test shows b parameters are non-zero, then x “Granger-causes” y
(special case of MVAR; see later)

## Slide 25: Directed, Nonlinear Measures
Generalised Synchronisation
Sensitive to Field-spread, Directed, Indirect, Nonlinear
D is the Euclidean distance between xt and embedded neighbours
Quian Quiroga et al (2000) Phys Rev E
m is the embedding dimension and l lag
Transfer Entropy (lagged generalisation of mutual information)
Immune to Field-spread, Directed, Indirect, Nonlinear
Schreiber (2000) Phys Rev Letters

## Slide 26: Talk Overview
1. Problem of Field Spread (Volume Conduction)
2. Linear vs Nonlinear measures
3. Directed vs Undirected measures
4. Direct vs Indirect measures
5. Generative Models

## Slide 27: Direct Measures
Multivariate Autoregressive Modelling (MVAR)
Various summary measures, eg,
Partial Directed Coherence (PDC):
Generalised form of Granger Causality
Though insensitive to true zero-lag dependencies (occur in reality?)
Baccala & Sameshima (2001) Biol Cybernet
Immune to Field-spread, Directed, Direct, Linear

## Slide 28: Talk Overview
1. Problem of Field Spread (Volume Conduction)
2. Linear vs Nonlinear measures
3. Directed vs Undirected measures
4. Direct vs Indirect measures
5. Generative Models

## Slide 29: Generative Models
Connectivity modelled between sources
Projected to sensors via headmodel
Typically a handful of sources, and a range of networks fit to data
Bayesian methods for comparing which network model is best
Dynamic Causal Modelling (DCM) is one approach
Chen et al, 2009, Neuroimage
Immune to Field-spread, Directed, Direct, Nonlinear, model-driven

## Slide 30
Measure | Immume to Field Spread | Directed | Nonlinear | Direct
Cross-Correlation | Y (l>0) | N | N | N
Coherence | Y (imaginary) | N | N | N
PLV/PLI | Y | N | N | N
Granger (bivariate) | Y | Y | N | N
Mutual Information | N | N | Y | N
Transfer Entropy | Y | Y | Y | N
Generalised Synchrony | N | Y | Y | N
MVAR (eg, PDC) | Y | Y | Y | N
Generative (eg, DCM) | Y | Y | Y | Y

## Slide 31
The End